## Slide 1
STUDENT TEMPLATE
Advanced IoT Systems
KLE Technological University • ECE Department
SENSE
PROCESS
COMMUNICATE
POWER
ACTUATE
Smart Coaster — Hydration Tracker
Notes: Template for student teams to document their IoT product teardown. Duplicate and fill in all placeholders.

## Slide 2
PROBLEM STATEMENT:
Most people fail to drink adequate water daily, leading to fatigue, headaches, and reduced cognitive performance. Existing hydration trackers require manual logging or smart bottles that are expensive and bottle-specific. No passive tracking solution exists for any cup or glass.
Notes: Fill in product details. Take a clean photo before disassembly.

## Slide 3
BLOCK DIAGRAM:
Map the product to the five IoT subsystems
SENSE
Sensors &
Transducers
→
PROCESS
MCU / SoC
& Memory
→
COMMUNICATE
Wireless
Radio
→
POWER
Supply &
Regulation
→
ACTUATE
Outputs &
Feedback
Actuate
Power
Communicate
Process
Sense
Load Cell Sensor( 1 KG)
OLED Display
BLE 5.0 GATT
App
HX711 24 bit ADC(5 Hz)
ESP 32
RTC (DS3231/DS1307)
→
→
→
→
1000mAh Lipo+TP4056 USB-C
Notes: Most important slide. Draw the architecture showing how 5 subsystems interconnect.

## Slide 4
Sense — Sensors & Transducers
Identify all sensing elements and their interfaces
1) Load Cell Sensor( 1Kg)
Why?
Converts weight into electrical signal
Works with any container (no fixed container needed)
Provides continuous weight measurement
Detects very small changes
Type : Load Cell / Weight Sensor
Capacity : 1 kg
Function: Measures the weight of the cup and water
Supply Voltage : 5V (via HX711)
Notes: For each sensor, read IC markings and find the datasheet. Include close-up photos of sensor ICs and their placement context on the board.

## Slide 5
Process — MCU / SoC & Memory
Identify the processing core, memory, and peripherals
2)HX711(24 Bit ADC)
Amplifies very small signal from load cell
Converts analog signal → digital data
Enables microcontroller to read weight values
Why?
Type:HX711 Load Cell Amplifier + ADC
Interface: I2C communication
3)RTC
Why?
Less clock drift
Easy to Interface (I2C Communication)
Which works easily with ESP32
Type : RTC Module
Function : Maintains time and triggers events like reset and reminders
Interface : I2C Protocol
Notes: Main MCU/SoC is usually the largest IC. Include photos showing the chip markings clearly and the surrounding decoupling/crystal circuit.

## Slide 6
4) ESP 32
Processes weight data from HX711
Performs sip detection & intake calculation
Supports BLE communication
Controls display, buzzer, and timer functions
Why?
Type :Microcontroller (ESP32 SoC)
Core :Dual-core processor
Function :Reads sensor data, processes logic, controls output devices, and manages communication
Interfaces :GPIO, I2C (OLED), SPI, UART, BLE
Notes: For each sensor, read IC markings and find the datasheet. Include close-up photos of sensor ICs and their placement context on the board.

## Slide 7
Communicate — Wireless & Connectivity
Identify wireless protocols, RF components, and antenna design
5)BLE 5.0 GATT
Type : Wireless Communication (BLE 5.0)
Function : Transfers intake data and alerts between ESP32 and mobile device
Range : ~10 meters
Frequency : 2.4 GHz
Why?
Enables wireless data transfer
Sends hydration data to mobile app
Supports low power operation
Provides real-time notifications
Notes: Photo the antenna structure and ground clearance zone. Show the radio IC markings clearly.

## Slide 8
Power — Supply & Regulation
Trace the complete power path from input to every rail
6) 1000mAh Lipo+TP4056 USB-C
Why?
Provides portable power supply
Supports rechargeable battery operation
Enables USB-C charging
Ensures continuous system operation
Type : LiPo Battery + Charging Module
Battery Capacity : 1000 mAh
Function : Supplies power to ESP32, HX711, OLED, and buzzer
Charging Module : TP4056 (USB-C input)
Notes: Photo the power section — regulators, inductors, capacitors. Show the input connector or battery area.

## Slide 9
Actuate — Outputs & Feedback
Identify all output and actuation elements
Type : OLED Display (I2C Interface)
Size : 0.96 inch (128 × 64 pixels)
Function : Displays intake data, progress bar, and system status
7) OLED
Low power consumption
Compact and light weight
Fast response time
Suitable for portable systems
Why?
Notes: Photo actuators — speakers, LEDs, motors, displays. Show driver ICs and their surrounding circuit.

## Slide 10
Schematic walkthrough: Analog ground strategy
I
Benefits Achieved
Reduced noise coupling
More stable readings
Better gram-level accuracy
Improved repeatability
Notes: Photo actuators — speakers, LEDs, motors, displays. Show driver ICs and their surrounding circuit.

## Slide 11
ERC report
I
The schematic design was verified using Electrical Rule Check (ERC) in Altium Designer.
All electrical connections, power nets, and signal paths were validated successfully.
The design meets all required electrical constraints and is ready for implementation.
Notes: Photo actuators — speakers, LEDs, motors, displays. Show driver ICs and their surrounding circuit.

## Slide 12
Software Architecture
1.Drivers

## Slide 13
2.Communication

## Slide 14
3.Algorithm

## Slide 16
Detailed Architecture

## Slide 17
Result Screenshots

## Slide 18
BOM:
S.No | Components | Specification | Quantity | Price
1 | ESP32 Dev Board | 3.3V, Dual-core, BLE + WiFi | 1 | ₹350 – ₹500
2 | Load cell | 5kg, Strain Gauge Type | 1 | ₹150 – ₹300
3 | HX711 Module | 24-bit ADC, Gain 128/64 | 1 | ₹80– ₹150
4 | OLED Display | 0.96”, 128×64, I2C | 1 | ₹120– ₹200
5 | RTC module | I2C, High accuracy, battery backup | 1 | ₹150– ₹250
6 | LiPo Battery | 3.7V, 1000mAh | 1 | ₹150– ₹300
7 | TP4056 Module | LiPo charger, Type-C/Micro USB | 1 | ₹50– ₹100
8 | PCB / Breadboard | Protype board | 1 | ₹100– ₹200
Notes: Photo actuators — speakers, LEDs, motors, displays. Show driver ICs and their surrounding circuit.

## Slide 19
S.No | Components | Specification | Quantity | Price
9 | LED | 3.3V compatible | 1 | ₹10– ₹30
10 | Resistors | 220Ω (for LED) | 2-3 | ₹1
11 | Connecting wires | Jumper wires | 1 set | ₹50– ₹100
12 | USB cable | Type-C / Micro USB | 1 | ₹50– ₹150

## Slide 20
Power Budget
I
Components | Voltage(V) | Current (mA) | Power(mW)
ESP32 (Active + BLE) | 3.3 | 80-150 | 264-495
ESP32 (Avg) | 3.3 | 80 | 264
ESP32 (Sleep) | 3.3 | 0.01-0.15 | 0.03-05
HX711 | 3.3 | 1.5 | 5
Load Cel | 3.3 | 1 | 3.3
OLED display | 3.3 | 15-25 | 50-82
RTC | 3.3 | 0.2 | 0.66
LED | 3.3 | 5-10 | 16.5-33
Notes: Photo actuators — speakers, LEDs, motors, displays. Show driver ICs and their surrounding circuit.

## Slide 21
Teardown Summary
Team Information
Team Name: Connective Minds
Topic : Smart Coaster Hydration
Members:
1. Aishwarya Y 01FE23BEC267
2. Nikhita Naik 01FE23BEC270
3. Sahana I G 01FE23BEC284
4. Vani S K 01FE23BEC285
Submission Checklist
Product overview with photo
System block diagram (5 subsystems)
Sense — ICs, interfaces, 3–4 features each
Process — MCU/SoC, memory, peripherals
Communicate — Protocol, antenna, RF details
Power — Full supply chain, regulators
Actuate — Outputs, drivers, feedback
Annotated PCB photos (front & back)
Complete component map with datasheets
Key learnings and observations
Notes: Every checklist item should be completed before submission.